## Slide 1: Introduction to Physical Science
Heat Capacity
Presented by Robert Wagner

## Slide 2: Heat
Heat is the spontaneous transfer of energy due to a temperature difference
  SI unit = Joule
Heat is often measure in calories
  1 calorie is the temperature needed to raise the temperature of 1.00 g of water by 1.00oC
More often used - kilocalorie
  This is what we call a Calorie when taking about food energy

## Slide 3: Mechanical Equivalent of Heat
Heat is a form of energy
Mechanical Equivalent of Heat
  The work needed to produce the same effects as heat transfer
  1.000 kcal = 4186 Joules
James Prescott Joule
  Experiment: Gravitational potential energy —> Kinetic Energy —> Heat
Image Credit: OpenStax College Physics - Figure 14.3 CC BY 4.0

## Slide 4: Heat and Phase Changes
When heat is added or removed from a system —> internal energy changes
  May increase/decrease temperature
  May involve a phase change

## Slide 5: Temperature Change and Heat Capacity
If there are no phase changes, the heat transfer depends on
  Change in temperature
  Mass of the system
  The substance and phase of the substance
  c = specific heat - amount of heat needed to raise the temperature of 1.00 kg by 1.00oC.
    SI unit:
    Also used:
Image Credit: OpenStax College Physics - Figure 14.4 CC BY 4.0

## Slide 6: Example
Image Credit: GRAN, CC BY 3.0 <https://creativecommons.org/licenses/by/3.0>, via Wikimedia Commons
An 0.500 kg aluminum pan is used to heat 0.250 liters of water from 20.0oC to 80.0oC. How much heat is required?
  Draw a sketch
  Identify known values
  Identify equation
  Enter values in the equation and solve

## Slide 7: Example
An 0.500 kg aluminum pan is used to heat 0.250 liters of water from 20.0oC to 80.0oC. How much heat is required?
  Draw a sketch
  Identify known values
  Identify equation
  Enter values in the equation and solve
Image Credit: GRAN, CC BY 3.0 <https://creativecommons.org/licenses/by/3.0>, via Wikimedia Commons
(See Table 14.1)

## Slide 8: Example
Image Credit: OpenStax College Physics - Figure 14.5 CC BY 4.0
Calculate the temperature increase of 100. Kg of brake material with an average specific heat of 800. J/kgoC if the material retains 10% of the energy from a 10,000. kg truck descending 75.0 m at a constant speed
  Draw a sketch
  Identify known values
  Identify equation
  Enter values in the equation and solve

## Slide 9: Example
Calculate the temperature increase of 100. Kg of brake material with an average specific heat of 800. J/kgoC if the material retains 10% of the energy from a 10,000. kg truck descending 75.0 m at a constant speed
  Draw a sketch
  Identify known values
  Identify equation
  Enter values in the equation and solve
Image Credit: OpenStax College Physics - Figure 14.5 CC BY 4.0

## Slide 10: Summary
Heat is the spontaneous transfer of energy due to a temperature difference
The Mechanical Equivalent of Heat relates energy in kilocalories to energy in Joules
The heat capacity of a substance tells how much energy is needed to raise the temperature of a kilogram of a substance by a degree Celsius